USB9

Ist ein USB Winkel-Ladestecker für kleine DIN Bordsteckdosen (SD14 oder BMW, Ducati, Triumph Serien-Bordsteckdosen) und setzt 12V auf USB-Standard  5V um. Max. bietet er eine Ladeleistung von 3A in Schnell-Ladefunktion (Quick Charge).

Durch die kompakte und gewinkelte Form lassen sich Ladekabel auch in seitlich verbaute Bordsteckdosen während der Fahrt einstecken. Durch die zusätzliche Gehäusehülle und einer Dichtung am Steckerhals ist Ladeadapter spritzwassergeschützt.

- Kompakte Winkelform

- 3A Powerlader QC Quickcharge

- Spritzwassergeschützt durch Gehäusehülle und Dichtung

- Geschütztes Produkt

USB9 is a 3A QC power charger for connect to various on-board DIN sockets (SD14 or BMW, Ducati, Triumph sockets) 12V to 5V USB standard. The right angle housing allows connecting plugs to side sockets while driving. The housing is splash proof.

- Small size – right angle shape

- 3 A power charger QC (Quick Charge)

- Splash proof

- Protected design

Technische Daten / product datas

Abmessungen / Dimensions 	L / B / H:	63 x 26 x 45 mm

Zolltarif-Nr. / Custom tarif no.	85444290	(Country: CN)

EAN-Code	4260258510966

Gewicht / Weight	30 g

Karton VPE / Package	100 St / Pcs